## Slide 1
ME2 - VCM on Raspberry Pi 5
Always listening locally · two scratch-trained TinyDSCNN-48 models
Speech-to-action path
01
Microphone + log-mel
16 kHz · 2.5 s · 40 × 251
→
02
Binary wake
NON_WAKE / WAKE_WORD
→
03
Intent classifier
31 fixed command classes
→
04
Coded action
Light · media · temp · weather
17,986 command clips
100 reference speaker IDs
524 personal saves
292 unique waveforms
74.9 KiB total
Two INT8 ONNX models
Notes: Source: deployment/current_vcm/metadata.json; docs/ME2_DATASET_ALIGNMENT.json; tinyvcm_antigrav/model.py. The 100 IDs are reference-dataset speaker IDs; personal recordings are dominated by one speaker. No LLM or ASR is used for recognition.

## Slide 2
Measured performance & demo
Reused speaker-held-out command split · fixed 0.95 wake operating point
97.1%
intent accuracy
97.1%
macro F1
8/8
personal wake hits
What the demo shows
1 Say “Hi Dandan” → wake gate opens
2 Control light, volume and local music
3 Set temperature; ask live weather
4 Switch microphone without restarting
Honest limits
Weakest class F1: 94.1%; 6 classes below 95% F1 or recall.
2 false wakes / 1855 non-wake clips at 0.95.
Latest pair is staged for a manual Pi test; live Pi speech remains unverified.
Notes: Source: deployment/current_vcm/metadata.json; runs/me2-vcm-20260930-refined-intent/final_evaluation.json. Wake counts are five-position offline saved-audio replay, not continuous room false activations. Reference test is reused; personal holdout shares speakers with training. The newest pair is not yet tested on the Pi.