## Slide 1
ME2 - VCM on Raspberry Pi 5
Always listening locally · two-stage TinyDSCNN-48 · no ASR
Two-stage offline speech-to-action
01
Mic + log-mel front end
16 kHz · 2.5 s · 40 × 251
→
02
Binary wake gate
2 classes · threshold 0.95
→
03
TinyDSCNN-48 intent
31 classes · 14,527 params
→
04
Coded action
Light · media · temp · weather
10,682 training rows
ME2 Spoken Command Dataset
4,418 frozen test clips
4,371 commands · 47 OOS
74.9 KiB total
Wake + intent INT8 ONNX
Notes: Source: the ME2 Spoken Command Dataset pinned revision a90b8d106349b02c5570a1a258503386043f63b2, the candidate training summary and the frozen comparison report. The candidate intent model was trained from random initialization; its separate binary wake model is byte-identical to the current model because this dataset contains no wake-positive examples. The local feature input is 16 kHz mono, 2.5 seconds, 40 by 251 log-mel. Recognition and commands run locally without ASR or an LLM.

## Slide 2
ME2 - VCM on Raspberry Pi 5
Frozen test · 4,371 supported + 47 OOS · one scoring pass
-0.69 pp
accuracy change · candidate
-0.35 pp
macro F1 change · candidate
0/47
candidate OOS false actions
Pi candidate trial
Candidate runs separately on Pi port 7865
Wake unchanged; intent retrained from scratch
Real-voice slices improve; synthetic score falls
No Pi mic, so live speech A/B is pending
Model choice
Only 2/31 candidate labels reach 95% F1; keep current default.
OOS actions: candidate 0/47; current live gate 22/47.
Current leads: 79.64% accuracy / 79.47% F1; candidate 78.95% / 79.12%.
Notes: One paired, frozen test pass scored 4,371 supported commands and 47 out-of-scope clips. Current raw accuracy and macro F1 were 79.64 percent and 79.47 percent; candidate values were 78.95 percent and 79.12 percent. The candidate performs better on the smaller real and varied source slices but worse on the large synthetic slice, so it is not promoted. At validation-selected gates, it made zero false actions on 47 out-of-scope clips with 61.36 percent correct-action coverage; the current deployed gate made 22 false actions on those 47 clips. The unchanged wake model made one false accept among 4,418 wake-negative clips; no wake-positive test rows exist. The Pi app is running separately at /home/dalmacio/Desktop/me2-dataset-candidate on port 7865, but there is no Pi microphone attached, so live speech remains untested.