## Slide 1
ME2 - VCM on Raspberry Pi 5
Always listening locally · two-stage TinyDSCNN-48 · no ASR
Two-stage offline speech-to-action
01
Mic + log-mel front end
16 kHz · 2.5 s · 40 × 251
→
02
Binary wake gate
2 classes · threshold 0.95
→
03
TinyDSCNN-48 intent
31 classes · 14,527 params
→
04
Coded action
Light · media · temp · weather
10,682 training rows
ME2 Spoken Command Dataset
202 live holdout clips
186 commands · 16 OOS
74.9 KiB total
Wake + intent INT8 ONNX
Notes: Updated benchmark reference: https://github.com/airimonda/vcm-benchmark. Architecture and active ME2 model details remain from the source deck. The latest cached public holdout contains 202 clips: 186 in-scope commands across 93 phrase variations, plus 16 out-of-scope clips.

## Slide 2
ME2 - VCM on Raspberry Pi 5
Raspberry Pi 5 Holdout Benchmark · 125 Evaluated Trials · On-Device INT8
71.6%
intent accuracy · 72.7% macro F1
97.7%
slot exact match · 100% timer/temp
6.3 ms
Pi 5 latency · 0.003 real-time factor
Benchmark Classification Accuracy
19-class intent accuracy: 71.6% [95% CI: 62.5%–79.2%]
93-variation command accuracy: 70.6% (macro F1: 72.7%)
Voice breakdown: 90.0% synthetic voice · 49.0% real voice
Wake gating: 100.0% detect rate · 0.0% false wake (0/16)
Raspberry Pi 5 Hardware & Runtime
Evaluated on deployed INT8 models (39.3 KB intent + 37.4 KB wake).
Inference: 6.3 ms mean (7.2 ms p95) · RTF 0.003 · Peak RAM 143 MB
Slots: 100% timer, temp, brightness, color; 85.7% alarm. Max temp 49°C.
Notes: This is the vcm-benchmark live Raspberry Pi procedure, not an offline replay of the 4,443-row Gold test. The latest cached holdout has 202 rows (186 supported command clips, 16 OOS, 93 variations). Full mode adds 16 in-scope no-wake false-wake controls, for 218 trials. Quick mode selects one clip per variation, all OOS clips, and 16 no-wake controls, for 125 trials. The full prior unscored generated plan averaged 4.396 seconds of played trial audio per trial, including wake word and silence; the SOP's mean random gap is 12.5 seconds. Therefore full timed phase = 218 x (4.396 + 12.5) / 60 = 61.4 minutes. Quick estimate uses the same prior generated plan's mean wake and no-wake trial lengths, producing 33.7 minutes. The tool recomputes and displays the run-specific estimate on its approval screen; mic check, log-format validation, three wake recordings and two unscored sound checks are extra and can take longer. The assistant must log intent, infer_ms and audio_ms. The Pi ME2 app was stopped at last post-cleanup verification and must be started intentionally; the isolated Gold candidate was removed. No benchmark trials were scored in this update. Source: https://github.com/airimonda/vcm-benchmark.