## Slide 1
ME2 - VCM on Raspberry Pi 5
Always listening locally · two-stage TinyDSCNN-48 · no ASR
Two-stage offline speech-to-action
01
Mic + log-mel front end
16 kHz · 2.5 s · 40 × 251
→
02
Binary wake gate
2 classes · threshold 0.95
→
03
TinyDSCNN-48 intent
31 classes · INT8 ONNX
→
04
Coded action
Light · media · temp · weather
10,682 training rows
ME2 Spoken Command Dataset
202 live holdout clips
186 commands · 16 OOS
74.9 KiB total
Wake + intent INT8 ONNX
Notes: Updated benchmark reference: https://github.com/airimonda/vcm-benchmark. Architecture and active ME2 model details remain from the source deck. The latest cached public holdout contains 202 clips: 186 in-scope commands across 93 phrase variations, plus 16 out-of-scope clips.

## Slide 2
ME2 - VCM on Raspberry Pi 5
Live Pi acoustic holdout · quick mode · 125 trials · INT8
36.7%
intent accuracy · 34.7% macro F1
33.9%
93-command accuracy · 32.2% macro F1
50%
false wake · 8/16 no-wake controls
Live Acoustic Benchmark Results
Intent accuracy: 36.7% [95% CI: 28%–46%] · macro F1 34.7%
93-command accuracy: 33.9% [95% CI: 26%–43%] · macro F1 32.2%
Intent by voice: 16.3% real (n=49) · 53.3% synthetic (n=60)
OOS false accept 62.5% (10/16) · false reject 36.6%
Pi 5 Acoustic & Runtime
Fifine mic check passed: SNR 21.8 dB. 109 wake-word clips + 16 no-wake controls.
Inference p95 9.3 ms · RTF p95 0.004 · max temperature 45.2 °C
Slot exact 88.0% (n=25). 40/109 no response; 49 extra fires. Response p95 6.99 s is provisional: 16/69 timings negative.
Notes: This is the vcm-benchmark live Raspberry Pi procedure, not an offline replay of the 4,443-row Gold test. The latest cached holdout has 202 rows (186 supported command clips, 16 OOS, 93 variations). Full mode adds 16 in-scope no-wake false-wake controls, for 218 trials. Quick mode selects one clip per variation, all OOS clips, and 16 no-wake controls, for 125 trials. The full prior unscored generated plan averaged 4.396 seconds of played trial audio per trial, including wake word and silence; the SOP's mean random gap is 12.5 seconds. Therefore full timed phase = 218 x (4.396 + 12.5) / 60 = 61.4 minutes. Quick estimate uses the same prior generated plan's mean wake and no-wake trial lengths, producing 33.7 minutes. The tool recomputes and displays the run-specific estimate on its approval screen; mic check, log-format validation, three wake recordings and two unscored sound checks are extra and can take longer. The assistant must log intent, infer_ms and audio_ms. The Pi ME2 app was stopped at last post-cleanup verification and must be started intentionally; the isolated Gold candidate was removed. No benchmark trials were scored in this update. Source: https://github.com/airimonda/vcm-benchmark.