## Slide 1
ME2 - Voice Controlled Smart Device
Always-on wake word + intent recognition at the edge
3 October 2026 | Live acoustic benchmark | Raspberry Pi 5 | 125 trials
Model and runtime
Mic 16 kHz -> 40-bin log-mel features
Wake gate -> 31-class INT8 intent model
Intent + slot -> local Raspberry Pi action
Model item
Value
Intent weights
15,971 params | 37.5 KB
Inference
7.9 ms mean | 9.3 ms p95
Live Pi 5 result
Metric
Measured
Intent accuracy
36.7% (40 / 109)
Command accuracy
33.9%
Out-of-scope false accepts
62.5% (10 / 16)
No-wake false fires
50.0% (8 / 16)
Evaluation set
Item
Value
Wake-positive trials
109
In-scope phrases
93 command variants
Out-of-scope clips
16
No-wake controls
16
Voice mix (scored)
49 real | 60 synthetic
Raspberry Pi 5
Runtime item
Value
Platform
4-core | 4 GB RAM
Inference RTF
0.003 mean | 0.004 p95
CPU temperature
45.2 C maximum
Throttling
None observed
Quick holdout benchmark; this evaluates the existing deployed ME2 model, not a retrained candidate.
p. 1 / 2
Notes: Source: official vcm-benchmark quick SSH run, 20261003-124806. Report and metrics: AI 231/Dumalaog_ME2 - Tiny Voice Command Model/archive/runs/class-benchmark-official-quick-20261003/20261003-124806/. The 109 wake-positive set comprises 93 in-scope phrase variants plus 16 out-of-scope items; 16 additional trials omit the wake word. Intent model inference metrics are model-only, not end-to-end response latency.

## Slide 2
Live acoustic benchmark
Metric
Overall
Real voice
Synthetic voice
Intent accuracy
36.7%
16.3%
53.3%
Command accuracy
33.9%
12.2%
51.7%
Intent macro F1
34.7%
12.0%
49.9%
Out-of-scope false accepts
10 / 16
Conflicted
Conflicted
Pi inference
Measure
Result
Intent inference
7.9 ms mean
Intent inference p95
9.3 ms
Real-time factor
0.003 mean / 0.004 p95
Peak CPU temperature
45.2 C
Interpretation
Recognition is the bottleneck
The model runs quickly on the Pi, but real-voice intent accuracy is only 16.3%. Overall false accepts were 10 of 16 out-of-scope clips.
The test logged 40 no-responses and 49 extra fires across 109 wake-positive trials.
Review before making model changes
1
Audit the acoustic event log: 16 of 69 response-latency samples are negative, so the reported 6.99 s p95 is provisional.
2
Repeat with a larger, balanced holdout and corrected event-to-utterance timing before claiming end-to-end latency or promoting a model.
125 trials total. FAR source breakdown conflicts in report prose; no retraining or promotion was performed.
p. 2 / 2
Notes: Source: official vcm-benchmark quick SSH run, 20261003-124806. Report: AI 231/Dumalaog_ME2 - Tiny Voice Command Model/archive/runs/class-benchmark-official-quick-20261003/20261003-124806/report.md; structured metrics in metrics.json. The benchmark records 69 response-latency samples, including negative values, making the 6.99 s response p95 unsuitable as a definitive end-to-end measure. Do not confuse the Pi model-inference timing (7.9 ms mean, 9.3 ms p95) with response latency. No retraining or candidate deployment occurred during this benchmark update.